## Slide 1: Razor Blade Witness
Peter Rose
Krich Group
April 12, 2017

## Slide 2: Outline
We present a new witness protocol, robust to some non-Condon effects
Pulse shapes and parameters
Define system parameters
Witness protocol and preliminary results
Additional technical details
What still needs to be done

## Slide 3: Outline
We present a new witness protocol, robust to some non-Condon effects
Pulse shapes and parameters
Define system parameters
Witness protocol and preliminary results
Additional technical details
What still needs to be done

## Slide 4: Start with a Bare Gaussian in Frequency Domain
(Zero frequency means resonant with the 0-0 ground state to excited state transition)

## Slide 5: Electric Field in Frequency Domain with Razor Blades
Razor Blade
Width
σrb
Razor Blade Center
ωrc
Gaussian Center
ωgc

## Slide 6: Electric Field Parameters
Pulse is characterized by 4 parameters
  Razor blade width – σrb (in frequency)
  Razor blade center - ωrc (in frequency)
  Gaussian sigma – σt (in time)
  Gaussian center - ωgc (in frequency)
For now we set ωgc = 0, i.e. to the 0-0 transition from the ground to the electronic excited state.

## Slide 7: Outline
Pulse shapes and parameters
Define system parameters
Witness protocol and preliminary results
Additional technical details
What still needs to be done

## Slide 8: Monomer (no coherence)
1 electronic excitation, 1 harmonic vibrational mode
Huang Rhys Factor – S
Linear Condon Violation – κ
  Defined relative to the condon dipole moment μ0:
    μ(R)=μ0(1+κR)
    R is the displacement from the ground state potential surface minimum
The ground state vibrational frequency – ωg = ω0
Excited state vibrational frequency – ωe = 0.9ω0

## Slide 9: Dimer (with coherence)
Two singly-excited electronic states, with coupling strength J.
ωe is the separation between excitonic states
No vibrations

## Slide 10: Outline
Pulse shapes and parameters
Define system parameters
Witness protocol and preliminary results
Additional technical details
What still needs to be done

## Slide 11: Fix the Gaussian Shape

## Slide 12: …And the razor blade width…
σrb = 10ω0

## Slide 13: …And vary the razor blade center
σrb = 10ω0

## Slide 14: Proposed Witness Protocol
  Choose pulses with ωgc = 0 and σrb> σt-1.
  Take pump-probe data S(T) as a function of delay time T for different values of ωrc.
  Take the Fourier transform of S(T) and extract the amplitude at ωe* for each value of ωrc.
  Plot the Fourier amplitudes as a function of ωrc.
*See slide entitled Additional Material Parameters for a note about this frequency

## Slide 15: Example of Protocol
  We show calculations for the following parameters:
    ωgc = 0
    σrb = 10ω0
    σt = 0.4ω0-1
  We vary ωrc from -8ω0 to 8ω0 in steps of ω0.
  We show calculations for a monomer with one vibrational mode, with several different values of S and κ.
  We compare these calculations to a system with electronic coherence at the same response frequency.

## Slide 16: Example of the Negative Witness
S = 0.1, κ = 0
Essence of witness is the peak to trough ratio
Peak
Trough
Monomer

## Slide 17: Some other examples
S = 0.1, κ = 0
S = 0.1, κ = 0.14
S = 0.1, κ = –0.04
Peak
Peak
Peak

## Slide 18: Example of the Positive Witness
Dimer

## Slide 19: Key Signature of Witness
Key qualitative difference: negative witness has at least one peak and a trough, whereas positive witness has no trough.
Dimer
Monomer

## Slide 20: When does it “work”
At large κ, the witness fails. Our goal is to determine what “large” is.
We consider a working witness protocol to be a case where the trough-to-peak ratio is <0.5.
For parameters (S, κ) where at least one peak exists with a trough-to-peak ratio <0.5, we consider that this is a working witness protocol.

## Slide 21: False Positive Witness
Monomer
S=0.1, κ=0.18
0.5 Failure Line
Here is an example of (S, κ) where the witness protocol fails.

## Slide 22: Working Region
0.5 Ratio Contour
Trough-to-peak ratio
This plot shows the trough-to-peak ratio for a variety of values of S and κ.
Witness protocol fails in this region
Witness protocol works in this region

## Slide 23: We can do better!
This is promising, because it suggests that there is a reasonable region of S-κ space where this witness protocol will work.
However, it is possible to improve this protocol by repeating the same procedure twice more with ωgc set to –1.5ω0 and +1.5ω0.

## Slide 24: Now change Gaussian center
If we change the Gaussian center, we can access a greater percentage of S-κ space.
A trough-like structure in any one of these experiments is interpreted as a negative witness.
ωgc= -1.5ω0
ωgc= 0
ωgc= 1.5ω0

## Slide 25: Outline
Pulse shapes and parameters
Define system parameters
Witness protocol and preliminary results
Additional technical details
What still needs to be done

## Slide 26: Additional Material Parameters
Fundamental Oscillation Frequency – f0
  In this presentation we set f0=200cm-1
  This is like a temperature knob, since we set the ambient temperature to be 300 Kelvin. For f0=100cm-1 we must calculate a boltzmann average over the lowest 15 initial ground vibrational states, whereas for f0=800cm-1 only the 0th mode of the initial ground state need be included.
Homogeneous Linewidth – Γ
  This is the decay rate of the oscillatory signal produced by the pump-probe experiment
  So far we have only studied Γ=0.1ω0, which means that the ground state and excited state frequencies cannot be distinguished for the given ratio of ωe/ωg = 0.9
Inhomogeneous Broadening
  We assume that the 0->0 transition frequency is actually a Gaussian distribution, so we calculate an incoherent average over 0->0 transition frequencies. As a general rule, as the inhomogeneous broadening increases, the region of the S-κ plane that is accessible using this technique decreases.
  In this presentation we set the σ of this Gaussian distribution to be 1ω0

## Slide 27: Spectroscopy Assumptions
We calculate the pump-probe signal assuming that the pump and probe pulses are identical (including in polarization)
All calculations assume that the pump and probe are well-separated in time even with the razor blades. Previous work done in the Condon approximation shows this to be a good assumption, despite the sinc-like quality of the pulses. However, we still need to verify that this holds for a system with a linear Condon violation.

## Slide 28: Outline
Pulse shapes and parameters
Define system parameters
Witness protocol and preliminary results
Additional technical details
What still needs to be done

## Slide 29: Next Steps
We must verify that these results hold when pump-probe overlap is taken into account.
Peter and Joey have been discussing some analytical work that needs to be completed about the S = 0 limit.
We need to consider a dimer model that includes two vibrational modes